## Slide 1: ROBOTIC HARDWARE SYSTEMS UGV : SUMMIT-XL STEEL MOBILE ROBOT
Muhammad Zulhafiz Bin Zulkifli
Muhammad Nazhan Bin Ramli
Muhammad Yusof Bin Mohamed Adam

## Slide 2
ROBOT BODY DESIGN
MOBILE ROBOT WITH MECHANICAL STEEL STRUCTURE
Dimensions 978 x 776 x 510 mm
Weight 105 kg
Payload 130 kg / 250 kg
Environment
Indoor
Enclosure class IP52 / IP64

## Slide 3
ACTUATORS & LOCOMOTIONS
The mobile platform has omnidirectional kinematics based on 4 high-power mechanum drive wheels. Each wheel integrates a brushless motor with a high precision odometer sensor.
Traction motors: 4 x 500 W brushless servomotors with safety brake

## Slide 4
NAVIGATION SYSTEM & CONTROLLER
Safety Laser Scanner - SICK microScan3
275° scanning angle
5.5 m field range

## Slide 5
NAVIGATION SYSTEM & CONTROLLER
Depth Camera - Intel Realsense D435
Closed-range navigation
Dynamic obstacle avoidance
Realtime video for teleoperation
Controller - JNF797-Q370
Embedded PC with Linux
i7, 8th Gen, 8GB RAM, 250GB M.2 SSD
ROS Architecture
Wheel Encoders
Built-in
Calculate odometry

## Slide 6
IMU - Vector Nav VN-100
IMU - Pixhawk
GPS - ZED-F9P module
NAVIGATION SYSTEM & CONTROLLER

## Slide 7
NAVIGATION SYSTEM & CONTROLLER

## Slide 8
DATA COLLECTION
Industrial Applications
Logistics
Surveillance & Monitoring
Research & Development

## Slide 9
DATA TRANSMISSION
WiFi
802.11 a/b/g/n/ac
Bluetooth 5.1
RS 232 Serial Communication
USB
RJ 45
Communication
Internal Connection
External Connection
Notes: WiFi and bluetooth to connect with the main system
RS 232 to connect with the LiDar Sensor
USB connect sensors
External connection - to add custom components easily

## Slide 10
POWER SYSTEM MANAGEMENT
LiFePO4
15/30 Ah @ 48VDC
Charging Process
Internal circuitry and a magnetic sensor
Adjustable voltage and can charge up to 800W
1.2 hours full charge (standard battery)
Autocentered feature using AR tag
Docking Station